I want a clean, modular, class-based Arduino code architecture for my hexapod robot system with the following features and hardware setup:

6 legs × 3 Dynamixel AX-18A servos (IDs 1 to 18), each leg identified as:

1: front-left with servo IDs 1,2,3

2: front-right with servo IDs 4,5,6

3: mid-left with servo IDs 7,8,9

4: mid-right with servo IDs 10,11,12

5: rear-left with servo IDs 13,14,15

6: rear-right with servo IDs 16,17,18

A turret with 2 AX-18A servos (pan ID 19, tilt ID 20) to rotate an AX-S1 sensor (ID 100)

OpenCR 1.0 board as the controller

Motors daisy-chained on OpenCR TTL port 1

BT-410 Bluetooth module connected to OpenCR UART1 port

RC100B remote control inputs received through BT-410

Remote Control parameters: speed, gait, direction, turret pan, turret tilt

Class-based code in separate Arduino files for maintainability

Code structure to be as follows
DynamixelController class:
  1. Handles communication with the Dynamixel servos on the TTL port
  2. Provides low-level servo control, ID-based commands
  3. Functions: setPosition, setSpeed, readPosition, initializeServos, etc.
2. Leg class:
  1. Represents a single leg (3 servos)
  2. Uses DynamixelController to control the leg servos
  3. Functions: setJointAngles, liftLeg, moveLegForward, etc.
3. Hexapod class:
  1. Aggregates 6 Leg instances
  2. Manages gait patterns and coordination between legs
  3. Functions: setGait, setSpeed, moveForward, moveBackward, turn, stop, etc.
4. Turret class:
  1. Controls the turret servos (pan ID 19, tilt ID 20)
  2. Aims the AX-S1 sensor
  3. Read AX-S1 sensor data
  4. Functions: rotateTurret, resetTurret, etc.
5. RCController class:
  1. Manages input from BT-410 (UART1)
  2. Parses RC100B remote commands
  3. Converts commands into actions (speed, direction, gait, turret pan, turret tilt)
  4. Functions: readInput, parseCommands, updateControlState
6. Main Arduino sketch
  1. Initializes all classes
  2. Runs main loop to update robot state based on RC commands

Additional notes:
- Use the official Dynamixel2Arduino library tailored for OpenCR to manage servos on TTL port 1.
- Add movement limits to all servos to avoid going beyond physical allowed angles.
- Communication with BT-410 will be UART1 on OpenCR. Need to set up Serial1 for this.
- Make sure to implement watchdogs or failsafe in case of lost RC signal.
- Gait and speed control should be designed for extensibility — possibly using state machines or lookup tables.
- Modularizing code into .h and .cpp files for each class to improve readability and maintenance.
- Help adapt code for PlatformIO.
- If you use millis(), it is declared in Arduino's core header.
- ROBOTIS Dynamixel2Arduino does not have setProfileVelocity() for AX-18A, AX-18A does not support velocity profiles, Use setGoalVelocity() instead.
- Provide final code in zip file